MicroStation V8 Seed Files

For V8 projects two files are used to organize all the base files that may be needed for the project.  The files will not be copied.  Models needed that are not already present in the project seed files will be imported.

- brgSeed.dgn – English file holding all seed models.

- brgMSeed.dgn – Metric file holding all seed models.

Project seed files will be used to begin a project.  These files contain the models needed to start the project and provide a base model to copy for other needed models.

- brgEngSheet.dgn – English project seed file contains:

  - Title English Sheet model named CCDDDDS000

  - Border English Info model named CCDDDDbdr

  - Detail Sheet Seed model named CCDDDDSSSS to copy for final plans

  - English Reference Work Sheet model named WorkingDetails to use for details to be scaled and referenced into the final plans

- brgMetSheet.dgn - Metric project seed file contains:

  - Title Metric Sheet model named CCDDDDS000

  - Border Metric Info model named CCDDDDbdr

  - Detail Sheet Seed model named CCDDDDSSSS to copy for final plans

  - Metric Reference Work Sheet model named WorkingDetails to use for details to be scaled and referenced into the final plans

- brgPreEngSheet.dgn – English project preliminary design seed file contains:

  - TSL Seed models named TSL_CC_DDD(D) to copy for TSL models provided at two different scales

  - Project Layout model named Structures for layout of structures for the design area

  - English Reference Work Sheet model named worksheet to use for details that may need to be match-lined to fit within border limits

  - Coordinates models provided in north or south state plane and SPSG:4269 – NAD83 coordinates for locating the latitude and longitude of a structure

- brgPreMetSheet.dgn - Metric project preliminary design seed file contains:

  - TSL Seed model named TSL_CC_DDDD to copy for TSL models

  - Project Layout model named Structures for layout of structures for the design area

  - Metric Reference Work Sheet model named worksheet to use for details that may need to be match-lined to fit within border limits